PipeLine Specifications

# No. 9700-FR Complete Fitness Route

FITNESS EQUIPMENT

Fitness equipment shall be PipeLine( Complete Fitness Route as manufactured by Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland OR 97201-3464 U.S.A.

GENERAL

Complete Fitness Route shall consist an introduction and instructional signs, directional sign posts and fitness apparatus manufactured in accordance with the following quality and design standards.  All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of fitness equipment.

1.0  SIGNAGE

Complete Fitness Route shall include one introduction sign, 18 station instructional signs and five directional sign posts.

1.1  Instructional and Introduction Signs

Each instructional sign shall consist of pipe frame and graphic panel.  One piece pipe frame shall be 1-5/16" (33 mm) o.d. schedule 40 steel pipe formed into a "U" shape.  Each frame leg shall embed 3'-0" (915 mm) below finished grade and have a 9/16" diameter hole to receive one No. 4 reinforcing bar (to be supplied by installing contractor).  Pipe frame shall be ground smooth, deburred, and CASPAX-7( finished in accordance with Section 4.0.

Each sign panel shall be fabricated of 18 gauge (1.2 mm) mild steel plate and include a graphic illustration and written instructions for safe and proper use of the fitness apparatus.  Panel shall be porcelain enamel finished BLUE or GREEN with white graphics in accordance with Paragraph 1.3.  The manufacturer shall attach panels to sign frames with vandal-resistant fasteners.

1.2  Directional Sign Posts

Each directional sign post shall consist of post and graphic panel.  Post shall be manufactured in accordance with Section 3.1 and be ground smooth, deburred, and CASPAX-7 finished in accordance with Section 4.0.

Each panel shall be 3-1/2" (102 mm) diameter and be fabricated of 20 gauge (1.2 mm) mild steel plate.  Panels shall be porcelain enamel finished BLUE or GREEN with white arrow in accordance with Paragraph 1.3.  The manufacturer shall attach panels to sign posts with vandal-resistant fasteners.

Directional sign post placement and orientation shall be made by the project architect or owner.

1.3  Signage Finish

Graphic panels shall be coated on all sides with porcelain enamel, a colorful, glossy, tough, extremely weather-resistant finish.  The porcelain enamel process shall permanently fuse a thick layer of glass to the metal substrate at temperatures exceeding 1,500(F (815(C).  To assure adhesion, only glasses possessing thermal expansion qualities lower than those of the steel plate shall be accepted.

2.0  FITNESS APPARATUS

Complete Fitness Route shall consist of 18 exercise stations.  See project plans for event sequence.

2.1  Heel-Flex

No. 9701 Heel-Flex station shall consist of one post and one instructional sign.

Post shall be 4-1/2" (o.d.) schedule 40 steel pipe in accordance with Section 3.1.  Six hand holds shall be permanently welded to post at graduated heights and be constructed of 1-5/16" (o.d.) schedule 40 steel pipe in accordance with Paragraph 3.5.  Ends of hand hold pipes shall be capped with cast aluminum caps. Instructional sign shall be in accordance with Section 1.0.

2.2  Toe-Reach

No. 9702 Toe-Reach station shall include twelve posts, assembly collars, twelve rails, four benches, and one instructional sign.

Posts shall be in accordance with Paragraph 3.1.  Assembly collars shall be in accordance with Paragraph 3.4.  Rails shall be in accordance with Paragraph 3.5.  Benches shall be in accordance with Section 5.0.  Instructional sign shall be in accordance with Section 1.0.

2.3  Toe-Touch

No. 9703 Toe-Touch station shall include one instructional sign in accordance with Section 1.0.

2.4  Knee-Grip

No. 9704 Knee-Grip station shall include one instructional sign in accordance with Section 1.0.

2.5  Straddle-Jump

No. 9705 Straddle-Jump station shall include one instructional sign in accordance with Section 1.0.

2.6  Hop-Over

No. 9706 Hop-Over station shall include three curved hop-over rails and one instructional sign.

Rails shall be 1-5/8" (o.d.) curved schedule 40 steel pipe.  Instructional sign shall be in accordance with Section 1.0.

2.7  Leg-Flex

No. 9707 Leg-Flex station shall include three posts at graduated heights and one instructional sign.

Posts shall be 4-1/2" (o.d.) schedule 40 steel pipe welded to 3/8" thick steel top plate.  Post shall be in accordance with Section 3.1.  Instructional sign shall be in accordance with Section 1.0.

2.8  Arm-Stretch

No. 9708 Arm-Stretch station shall include four posts, assembly collars, four rails, three pairs of rings at graduated heights, chain, and instructional sign.

Posts shall be in accordance with Paragraph 3.5.  Assembly collars shall be in accordance with Paragraph 3.4.  Rails shall be in accordance with Paragraph 3.5.  Triangular rings shall be cast aluminum alloy.  Chain shall be galvanized 1/4" proof coil chain.  Instructional sign shall be in accordance with Section 1.0.

2.9  Body-Tuck

No. 9709 Body-Tuck station shall include twelve posts, assembly collars, twelve rails, four benches and one instructional sign.

Posts shall be in accordance with Paragraph 3.5.  Assembly collars shall be in accordance with Paragraph 3.4.  Rails shall be in accordance with Paragraph 3.5.  Benches shall be in accordance with Section 5.0.  Instructional sign shall be in accordance with Section 1.0.

2.10  Body-Pull

No. 9710 Body-Pull station shall include four posts, assembly collars, four rails at graduated heights and one instructional sign.

Posts shall be in accordance with Paragraph 3.5.  Assembly collars shall be in accordance with Paragraph 3.4.  Rails shall be in accordance with Paragraph 3.5.  Instructional sign shall be in accordance with Section 1.0.

2.11  Leg-Kick

No. 9711 Leg-Kick station shall include one instructional sign in accordance with Section 1.0.

2.12  Vault-Over

No. 9712 Vault-Over station shall include one vaulting rail and one instructional sign.

Curved vaulting rail shall be 1-5/8" (o.d.) schedule 80 steel pipe.  Instructional sign shall be in accordance with Section 1.0.

2.13  Sit-Up

No. 9713 Sit-Up station shall consist of two foot rails, back rail, two benches and one instructional sign.

Foot rails shall be curved 1-5/8" (o.d.) schedule 40 steel pipe.  Back rail shall be curved 2-3/8" (o.d.) schedule 40 steel pipe.  Benches slat shall be in accordance with Sections 5.0 or 6.0. Bench frames shall be fabricated from 2-1/2" x 2-1/2" x .120" thick wall square mild steel seamless tubing and 3/8 inch thick mild steel plate.

Instructional sign shall be in accordance with Section 1.0.

2.14  Push-Off

No. 9714 Push-Off station shall consist of four posts, assembly collars, three rails at graduated heights and one instructional sign.

Posts shall be in accordance with Paragraph 3.5.  Assembly collars shall be in accordance with Paragraph 3.4.  Rails shall be in accordance with Paragraph 3.5.  Instructional sign shall be in accordance with Section 1.0.

2.15  Leg-Over

No. 9715 Leg-Over station shall consist of three posts at graduated heights, one bench and one instructional sign.

Posts shall be in accordance with Paragraph 3.5.  Benches shall be in accordance with Section 5.0.   Bench frames shall be fabricated from 2-1/2" x 2-1/2" x .120" thick wall square mild steel seamless tubing and 3/8 inch thick mild steel plate.  Instructional sign shall be in accordance with Section 1.0.

2.16  Arm-Walk

No. 9716 Arm-Walk station shall consist of two handrails and one instructional sign.

Handrails shall be curved 1-7/8” (o.d.) schedule 40 steel pipe.  Instructional sign shall be in accordance with Section 1.0.

2.17  Hip-Flex

No. 9717 Hip-Flex station shall consist of four posts, assembly collars, three rails at graduated heights and one instructional sign.

Posts shall be in accordance with Paragraph 3.5.  Assembly collars shall be in accordance with Paragraph 3.4.  Rails shall be in accordance with Paragraph 3.5.  Instructional sign shall be in accordance with Section 1.0.

2.18  Beam-Walk

No. 9718 Beam Walk station shall consist of one curved beam and one instructional sign.

Beam shall be constructed of 2" x 3" x .180" thick wall rectangular mild steel  welded to 2-3/8" (o.d.) schedule 40 steel pipe legs.  Instructional sign shall be in accordance with Section 1.0.

3.0  METAL MATERIALS

3.1  Posts

All posts shall be 4-1/2" (o.d.) schedule 40 steel pipe with a minimum wall thickness of 7/32" in accordance with ASTM A-53, Type E, Grade A.  Thin wall tubing is not acceptable.  Posts and their end caps shall be CASPAX-7( finished in accordance with Section 4.0.

3.2  End Treatment

Exposed ends of posts shall be fitted with a cast aluminum (384 alloy) hemi-dome end cap permanently adhered in place.  Easily vandalized plastic and/or friction fit end caps are not permitted.

3.3  Post Embedment

Posts shall be embedded 3’-0" (915 mm) below grade in concrete footings as depicted on the erection drawings. Actual concrete footing sizes can vary and depend on job site and climatic conditions.  Consult project engineer/owner for exact requirements.  Posts shall include through holes to receive two No. 4 reinforcing bars (to be supplied by installing contractor).

Separate bench frames and smaller pipe apparatus shall be embedded 1’-6” (460 mm) below grade except for Arm-Walk which shall be embedded 3’-0” (915 mm) below grade.

3.4  Collars

Cast aluminum (384 alloy) two-piece attachment collars shall be provided in sufficient quantity to connect all rails to support posts.  Collars must be formed to recess bolt fastener.  Each collar set shall include two vandal-resistant stainless steel socket-head cap screws with nuts and two 1/4" x 1" drive rivets.  Collars shall be CASPAX-7 finished in accordance with Section 4.0.

3.5  Straight and Curved Rails

Unless otherwise noted, all steel straight and curved rails shall be 1-5/16" (33 mm) o.d. schedule 40 steel pipe in accordance with ASTM A-53, Type E, Grade A.  Straight and Curved Rails shall be CASPAX-7 finished in accordance with Section 4.0.

3.6  Fabrication

All welds shall comply with AWS standard D1.1.  All edges, ends, and welds shall be ground smooth by hand to a maximum grit of 36 and shotblasted to a uniform surface texture.

3.7  Quality Control

Inspectors shall examine metal components for correct fabrication, fastener hole alignment, and smoothness.

3.8  Additional Hardware

Additional hardware shall be provided in sufficient quantity to complete assembly of the PipeLine Fitness Clusters.  All hardware shall be non-ferrous, or color finished with CASPAX-7, or galvanized, or electrostatic zinc plated in accordance with the manufacturer's standard.

4.0  METAL FINISH

Metal parts, except fasteners and sign panels, shall be finished with CASPAX-7, a colorful, tough, opaque, exterior use powder coating.  Liquid, epoxy, or lead-containing powder coatings are not acceptable.  The CASPAX-7 color shall be the manufacturer's standard or as selected by the owner's representative and designated on the project plans and/or specifications.

4.1 Cleaning

Substrate preparation shall consist first of mechanical cleaning to remove heavy mill scale, rust, varnish, grease, etc., then chemical cleaning in accordance with TT-C-490C, Methods I and III.

4.2  Phosphate Application

After cleaning, the metal substrate shall receive a corrosion-inhibiting iron phosphate coating in accordance with TT-C-490C, Type II, before application of the final color coat.

4.3  Powder Application

The coating powder shall be uniformly applied by the electrostatic method to a minimum thickness of six mils.  Promptly after the application of the powder, the coating shall be oven-cured at 400(F (204(C) to chemically bond the finish to the substrate and to render the color finished surface resistant to abrasion, impact, household chemicals, weathering and rusting.

4.4 Chronological Importance

For a corrosion-inhibiting agent to be effective, all fabrication including cutting, coping, grinding, and welding must be completed before application of the corrosion-inhibiting agent.  Corrosion-inhibiting agent applied prior to fabrication are not acceptable.

4.5  Quality Control

The applicator shall test the finish of each lot for correct millage, chemical resistance,  hardness, and internal bond in accordance with established industry standard test methods.

Records of this quality control procedure shall be made and retained for two years.

5.0  TIMBER MATERIALS

All fitness equipment wood components shall be manufactured from Playground Equipment Grade Douglas fir timbers, selected by the equipment manufacturer for strength, durability, and appearance.

5.1  Playground Equipment Grade

Timber benches shall be Coastal Douglas fir (Pseudo-tsuga menziesii), free-of-heart-center (F.O.H.C.).  To assure long, useful life, timbers containing the heart center or pith of the log shall not be accepted.

5.2  Timber Characteristics

All timbers shall be fine-grained, with at least 80 percent of the pieces possessing eight annular rings to the inch, the remainder having at least six rings to the inch.  There shall be no loose knots, knotholes, shake, unsound wood, white specks or honeycomb allowed.  To eliminate slivering, timbers shall be free of wane, and planer skips are not allowed in dressing. Except as noted, other characteristics and limiting provisions are in accordance with Paragraph 131-A Standard Grading Rules for West Coast Lumber.

5.3  Chronological Importance

To effectively receive pressure preservative treatment of the timber materials, all fabrication, including sawing, notching, and drilling, shall be completed prior to preservative treatment.

5.4  Wood Preservation

All wood components shall be pressure-preservatively treated with a water repellant formulation designed for use on fitness equipment.  Preservatives containing arsenic, pentachlorophenol, creosote or similar toxic chemicals as their active ingredient shall not be used.

5.5  Composition

The preservative solution shall be homogeneous and capable of deep penetration, not merely an emulsion.  The treatment shall not materially change the color of the wood to which it is applied.

5.6  Application

Wood shall be pressure impregnated by the closed cylinder, vacuum pressure method as prescribed by the latest standards for the American Wood Preservers' Association.  The preservative carrier shall conform to AWPA Standard C1 (latest edition).

5.7  Verification

Accordance to the requirements of this specification shall be monitored by an independent inspection agency in accordance with established industry quality control and inspection procedures.

5.8  Quality Control

Inspectors shall examine each timber component for correct fabrication, fastener hole alignment, and for smooth end, edge, and face treatment.  All play equipment wood components shall be manufactured from Playground Equipment Grade Douglas fir timbers, selected by the equipment manufacturer for strength, durability, and appearance.

6.0  INSTALLATION INSTRUCTIONS AND AIDS

To guide installation, each PipeLine Complete Fitness Route shall be accompanied by bills of materials, written instructions, and an erection plan view drawing to be furnished prior to or with the delivery of the fitness equipment.  To facilitate assembly, each part shall be indelibly stenciled with an easily-read identification number keyed to the bills of materials and erection drawings.  All components shall be shipped unitized, protectively wrapped, banded for mechanical handling and ready for assembly.