PipeLine Specifications

# No. 9714 Push-Off Station

FITNESS EQUIPMENT

Fitness equipment shall be PipeLine( No. 9714 Push-Off as manufactured by Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland OR 97201-3464 U.S.A.

GENERAL

Push-Off station shall consist of four posts, assembly collars, three rails at graduated heights and one instructional sign manufactured in accordance with the following quality and design standards.  All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of fitness equipment.

1.0  SIGNAGE

1.1  Instructional Sign

Instructional sign shall consist of pipe frame and graphic panel.

One piece pipe frame shall be 1-5/16" (33 mm) o.d. schedule 40 steel pipe formed into a "U" shape.  Each frame leg shall embed 3'-0" (915 mm) below finished grade and have a 9/16" diameter hole to receive one No. 4 reinforcing bar (to be supplied by installing contractor).  Pipe frame shall be ground smooth, deburred, and CASPAX-7( finished in accordance with Section 4.0.

Sign panel shall be fabricated of 18 gauge (1.2 mm) mild steel plate and include a graphic illustration and written instructions for safe and proper use of the fitness apparatus.  Panel shall be porcelain enamel finished BLUE or GREEN with white graphics in accordance with Paragraph 1.3.  The manufacturer shall attach panels to sign frames with vandal-resistant fasteners.

1.3  Signage Finish

Graphic panel shall be finished on all sides with porcelain enamel, a colorful, glossy, tough, extremely weather-resistant finish.  The porcelain enamel process shall permanently fuse a thick layer of glass to the metal substrate at temperatures exceeding 1,500(F (815(C).  To assure adhesion, only glasses possessing thermal expansion qualities lower than those of the steel plate shall be accepted.

2.0  FITNESS STATION

2.14  Push-Off

Posts shall be 4-1/2" (o.d.) schedule 40 steel pipe in accordance with Section 3.1. Assembly collars shall be in accordance with Section 3.4 and pipe rails shall be constructed of 1-5/16" (o.d.) schedule 40 mild steel pipe manufactured in accordance with Section 3.0 and CASPAX-7 finished in accordance with Section 4.0.  Instructional sign shall be in accordance with Section 1.0.

3.0  METAL MATERIALS

3.1  Posts

All posts shall be 4-1/2" (o.d.) schedule 40 steel pipe with a minimum wall thickness of 7/32" in accordance with ASTM A-53, Type E, Grade A.  Thin wall tubing is not acceptable.  Posts and their end caps shall be CASPAX-7( finished in accordance with Section 4.0.

3.2  End Treatment

Exposed ends of posts shall be fitted with a cast aluminum (384 alloy) hemi-dome end cap permanently adhered in place.  Easily vandalized plastic and/or friction fit end caps are not permitted.

3.3  Post Embedment

Posts shall be embedded 3’-0" (915 mm) below grade in concrete footings as depicted on the erection drawings. Actual concrete footing sizes can vary and depend on job site and climatic conditions.  Consult project engineer/owner for exact requirements.  Posts shall include through holes to receive two No. 4 reinforcing bars (to be supplied by installing contractor).

3.4  Collars

Cast aluminum (384 alloy) two-piece attachment collars shall be provided in sufficient quantity to connect all rails to support posts.  Collars must be formed to recess bolt fastener.  Each collar set shall include two vandal-resistant stainless steel socket-head cap screws with nuts and two 1/4" x 1" drive rivets.  Collars shall be CASPAX-7 finished in accordance with Section 4.0.

3.5  Straight and Curved Rails

Except as noted, all pipe rails shall be schedule 40 steel pipe in accordance with ASTM A-53, Type E, Grade A.  Thin wall tubing is not acceptable.  Steel plate shall be in accordance with ASTM A-36.  All steel parts shall be CASPAX-7( finished in accordance with Section 4.0.

3.6  Fabrication

All welds shall comply with AWS standard D1.1.  All edges, ends, and welds shall be ground smooth by hand to a maximum grit of 36 and shotblasted to a uniform surface texture.

3.7  Quality Control

Inspectors shall examine metal components for correct fabrication, fastener hole alignment, and smoothness.

3.8  Additional Hardware

Additional hardware shall be provided in sufficient quantity to complete assembly of the PipeLine Fitness Station.  All hardware shall be non-ferrous, or color finished with CASPAX-7, or galvanized, or electrostatic zinc plated in accordance with the manufacturer's standard.

4.0  METAL FINISH

Metal parts, except fasteners and sign panels, shall be finished with CASPAX-7, a colorful, tough, opaque, exterior use powder coating.  Liquid, epoxy, or lead-containing powder coatings are not acceptable.  The CASPAX-7 color shall be the manufacturer's standard or as selected by the owner's representative and designated on the project plans and/or specifications.

4.1 Cleaning

Substrate preparation shall consist first of mechanical cleaning to remove heavy mill scale, rust, varnish, grease, etc., then chemical cleaning in accordance with TT-C-490C, Methods I and III.

4.2  Phosphate Application

After cleaning, the metal substrate shall receive a corrosion-inhibiting iron phosphate coating in accordance with TT-C-490C, Type II, before application of the final color coat.

4.3  Powder Application

The coating powder shall be uniformly applied by the electrostatic method to a minimum thickness of six mils.  Promptly after the application of the powder, the coating shall be oven-cured at 400(F (204(C) to chemically bond the finish to the substrate and to render the color finished surface resistant to abrasion, impact, household chemicals, weathering and rusting.

4.4 Chronological Importance

For a corrosion-inhibiting agent to be effective, all fabrication including cutting, coping, grinding, and welding must be completed before application of the corrosion-inhibiting agent.  Corrosion-inhibiting agent applied prior to fabrication are not acceptable.

4.5  Quality Control

The applicator shall test the finish of each lot for correct millage, chemical resistance,  hardness, and internal bond in accordance with established industry standard test methods.

Records of this quality control procedure shall be made and retained for two years.

7.0  INSTALLATION INSTRUCTIONS AND AIDS

To guide installation, each No. 9714 Push-Off station shall be accompanied by bills of materials, written instructions, and erection drawings to be furnished prior to or with the delivery of the fitness equipment.  To facilitate assembly, each part shall be indelibly stenciled with an easily-read identification number keyed to the bills of materials and erection drawings. All components shall be shipped unitized, protectively wrapped, banded for mechanical handling and ready for assembly.